## Slide 1
Concept

## Slide 2
PROJECT
PART NAME
PART NO.
TYPE
DATE
----
CUSTOMER NAME
Guard_Assy.Side Sill_Splas
77230-58000
Checking Fixture
19-12-2024

## Slide 3
Part Images
A Surface
B Surface

## Slide 4
Resting & Locking
A-A
A
Part Hole Size:-Ø9mm
Pin Size:- Ø8.9mm
Thread pin will be provided to rest and lock the part at 1 place as per drawing tolerance as shown above.
A
Part
Thread Pin
Bush(Resting)
Base Plate
Stand

## Slide 5
Locking
B-B
One side locking mechanism will be provided as per surround to lock the part at 2 places as shown above.
B
Part
Base Plate
Stand
B
Mechanism

## Slide 6
Resting & Locking
C-C
Clutch operated mechanism will be provided as per surrounding to lock and rest the part at 07 places as shown above.
C
Part
Base Plate
C
Mechanism

## Slide 7
Resting & Locking
D-D
The drawing and CAD model do not match; a hole shown in the drawing is missing in the CAD model
D
D
Thread pin will be provided to rest and lock the part at 1 place as per drawing tolerance as shown above.
Part
Thread Pin
Bush(Resting)
Base Plate
Stand
Part Hole Size:-Ø7mm
Pin Size:- Ø6.9mm

## Slide 8
Resting & Locking
F-F
F
Part Hole Size:-Ø16mm
Pin Size:- Ø15.8mm
Thread pin will be provided to rest and lock the part as per drawing tolerance as shown above.
Part
Thread Pin
Bush(Resting)
Base Plate
Stand
F

## Slide 9
Resting & Locking
J-J
J
Part Hole Size:-Ø9.6mm
Pin Size:- Ø9.6mm
Thread pin will be provided to rest and lock the part as per drawing tolerance as shown above.
J
Thread Pin
Base Plate
Stand
Part

## Slide 10
Resting & Locking
L-L
L
Part Hole Size:-5x7
Pin Size:- Ø4.9mm
Thread pin will be provided to rest and lock the part as per drawing tolerance as shown above.
L
Thread Pin
Base Plate
Stand
Part

## Slide 11
Resting & Locking
M-M
M
M
Mechanism and thread pin will be provided as shown above
Mechanism
Base Plate
Stand
Thread Pin
Part

## Slide 12
Resting & Locking
N-N
N
Part Hole Size:-Ø8mm
Pin Size:- Ø7.9mm
Thread pin will be provided to rest and lock the part at 1 place as per drawing tolerance as shown above.
N
Part
Thread Pin
Base Plate
Stand

## Slide 13
Resting & Locking
P-P
P
Part Hole Size:-Ø10mm
Pin Size:- Ø9.9mm
Thread pin will be provided to rest and lock the part at 1 place as per drawing tolerance as shown above.
P
Part
Thread Pin
Base Plate
Stand

## Slide 14
Gap Flush
Q-Q
Swing template will be provided with 3mm gap and 0 mm flush and Body will be provided with 3mm gap and 0,3 mm trimline as shown above.
Q
Q
Body
Base Plate
Part
0
3
3
Stand
Swing Template

## Slide 15
Gap Flush
R-R
Gap and Flush body will be provided all around the part with 3mm gap and 0 mm flush as shown in above image.
R
Body
Part
R
Base Plate
Body
Part
3
S-S
S
S
3
Base Plate

## Slide 16
Fixture Orientation
Isometric
Top
Side
Front

## Slide 17
Thank You